## Slide 1
1. SYSTEM ARCHITECTURE FLOWCHART — STM32H723ZG (550 MHZ)
End-to-End Drive-by-Wire Signal Flow & Plain-English Guide
High-Level Compute
STM32H723ZG Controller (100 Hz Loop)
Vehicle Plant
NVIDIA Jetson / Host PC (ROS 2 / Autoware / Python GUI)
Plain English — The AI Brain: Decides path & speed; sends 16B command (0x01) & receives 26B status (0x81) at 50 Hz.
Binary Frame Envelope (protocol.c): SOF: 0xAA 0x55 ¦ CRC-16-CCITT: 0x1021 (Init 0xFFFF) CMD (0x01, 16B): dir, steer_angle (±30°), accel (0-100%), brake, estop. TLM (0x81, 26B @ 50Hz): state, actual_angle, pot_v, effort, DAC_v, link.
Circular DMA UART (CRC-16 + 200ms WDG)
State Executive (INIT / CALIB / ACTIVE / FAULT)
Plain English — 100 Hz Reflex Center: • Zero-CPU RX: DMA1_Stream1 reads bytes in background. • 200ms Watchdog: Auto-cuts throttle & applies 1.65V brake if link drops. • TIM6 10ms Tick: Orchestrates all 8 App/ libraries deterministically.
Extended Kalman Filter (EKF) (Pos & Velocity)
Steering PID Controller (D-on-Measurement)
Drivetrain Feedforward (DAC1 Thr & Brk)
aev_live Watch (100Hz CubeIDE)
Steering Rack Potentiometer (Feedback Eye)
Cytron MDD10A Steering Motor (±60% Cap)
Main Traction Motor Ctrl (Pure Analog)
Brake Actuator / Relay (1.65V / 3.3V)
Framed UART 115200 8N1 (PD8/9)
ADC1 IN15 (PA0) 0.15–3.15V Pot
TIM3 PWM (PC6) + DIR (PD14) 550Hz
DAC1 CH1 (PA4) 0.0–3.3V Analog
DAC1 CH2 (PA5) 0.0–3.3V Analog

## Slide 2
2. MOTION CONTROL & SENSOR FUSION — APP/MOTIONCONTROL & APP/SENSORS
How the Car Teaches Itself Steering Limits and Filters Out Noise
1. Self-Teaching Steering Calibration
1. Sweep Right (+45%) CAL_STATE_SWEEP_DIR_1
2. Back Off (-45%) 500 ms Gear Relief
3. Sweep Left (-45%) CAL_STATE_SWEEP_DIR_2
4. Compute Map Center, Span & Polarity
5. Center & Prime EKF Within 30mV -> ACTIVE
Windowed Stall Detection: • 600ms startup grace. • 100ms window checks ¦ΔV¦ ≤ 5mV for 500ms. • No physical switches!
Auto-Polarity (Stops Runaway): • If limit_1 > limit_2: polarity_sign = +1 • Else: sign = -1 • Fixes reversed wires!
On-Demand Reset: Press Blue Button B1 (PC13) anytime.
2. Noise Rejection & Kalman Filter
Stage 1: 16-Bit ADC DMA Oversampling (PA0) DMA1_Stream0 averages 64 raw samples (0–65535) every 10ms.
Stage 2: Exponential Moving Average (α = 0.20) y_bar = 0.20*y_block + 0.80*y_prev -> V_pot = (y_bar/65535)*3.3V
EKF Predict (100Hz) x0 += x1 * 0.01s x1 += ((u - x1)/τ)*0.01s P = F*P*F' + Q
EKF Update (Gain K) y = z - x0 K = P*H'/(H*P*H' + R) x += K*y (Zero Lag!)
Plain English — Why Use a Kalman Filter? Simple speed math ((V_now - V_last) / 0.01s) multiplies electrical noise by 100x, making the steering motor buzz and jerk. The EKF predicts smooth, zero-lag velocity!
3. Smooth PID & Actuator Clamps
Derivative-on-Measurement PID (pid.c) u(t) = 5.0 * e(t) + 1.0 * ∫e dt - 0.20 * y_dot_EKF(t) Plain English: Damps using EKF speed so step targets never cause 'derivative kick'!
End-Stop Soft Clamps & Current Protection Within 40 mV of left/right limits, outward effort is clamped to 0.0f. Plain English: Stops motor before hitting metal hardstops (blocks 15–30A+ burnout).
Steering Output: TIM3 PWM (PC6) + DIR (PD14) 550 Hz PWM capped at ±60% active duty (anti-windup ±0.25); 0% if link drops.
Traction & Brake: Open-Loop 12-Bit DACs (PA4 / PA5) 0–4095 counts -> pure 0.0–3.3V analog (no PID needed; EV controller regulates speed).

## Slide 3
3. SUPERVISORY LOOP, SAFETY & TESTING
100 Hz Execution Flowchart, Failsafes & Quick-Start
1. 100 Hz TIM6 Loop
TIM6_DAC_IRQHandler (10 ms) -> App_Step_100Hz() Check PC13 Button -> Read DMA UART & 16-Bit ADC
CALIB (1) Sweep ±45% Lock Thr 0V Green 5 Hz
ACTIVE (2) EKF + PID DACs 0-3.3V Green 1 Hz
FAULT (3) Thr 0V, Steer 0% Brake 3.3V Red Blinks
Update aev_live Struct (100 Hz) & Traffic-Light LEDs Every 2nd tick (50 Hz / 20ms): Broadcast 26B Binary Telemetry (0x81)
CubeIDE Live Watch (extern volatile VehicleLiveMonitor_t aev_live): • command: drive_direction, steer_angle, acceleration, brake, estop • steering & drivetrain: target/actual deg, pot_v, effort, throttle/brake DAC • calibration & safety: center/limit_v, state, link_alive, watchdog_ms, error
2. Safety Matrix & LED Codes
8 Automatic Hardware & Software Safety Layers: L1 Boot Safe (0ms): DACs 0V, PWM 0%, DIR low on startup. L2 Watchdog (≤200ms): Packet loss -> 0V thr, 1.65V brake, 0 steer. L3 E-Stop (≤10ms): estop != 0 latches 3.3V emergency brake & 0V thr. L4 Pot Bounds (≤10ms): <0.15V or >3.15V (broken wire) disables drive. L5–L8 Motor Guards: 40mV stop clamp, ±1 auto-polarity, ±60% cap, 10s timeout.
Traffic-Light LEDs (PB0, PE1, PB14) — Non-Blocking 100 Hz: Green LD1 (PB0): 5 Hz flash = Calibrating (stay clear); 1 Hz = Active. Yellow LD2 (PE1): 10 Hz flash = Link alive (≤200ms); 1s burst = 1 packet. Red LD3 (PB14) Diagnostic Blink Codes (200ms pulse + 1.2s pause): 1 Blink = COMM_TIMEOUT ¦ 2 Blinks = CALIBRATION_FAIL 3 Blinks = SENSOR_BOUNDS ¦ 4 Blinks = ESTOP ¦ Solid = FATAL
3. Quick-Start & Porting
Step 1: Build & Flash Firmware • CubeIDE: Select project & press Ctrl+B. • CLI: cd Debug && make -j8 all
Step 2: Launch Python Ground GUI • Run: python App\Testing\aev_diagnostic_gui.py • Connect ST-Link COM (115200 8N1), click Start 50 Hz Streaming, drag Steer/Throttle.
Step 3: HTerm Raw HEX Verification • Neutral: AA55 0101 ... 4E83 55AA • +10°/15%: AA55 0102 ... 59A2 55AA • E-Stop: AA55 0103 ... 1C52 55AA
Porting UART (protocol.c): Enable USARTx Circular DMA in CubeMX .ioc & set #define COMM_UART huartX.